DenseNet & CTC
RNN-free architecture for text recognition
GMO – 08/07/2020
Thanh Chu

---
Overview
Introduction
Dense Networks
Architecture
Connectionist Temporal Classification
Q & A

---
Introduction

---
Introduction
Dense Networks or DenseNets
One of the best performances on CIFAR-10, CIFAR-100, SVHN and ImageNet with less computation
By Gao Huang et. al. ‘Densely Connected Convolutional Networks’ 2017

---
History of CNN architectures

---
Comparison with ResNet
DenseNet-BC (Bottle-Neck)

---
Comparison with ResNet
Same accuracy – less parameters/flops

---
Dense Networks

---
Basics
- Convolution, BatchNorm, ReLU, MaxPooling
- Dense + Transition
- AveragePooling, Linear

---
Dense Block
- Dense block with 5 layers
- Growth rate k = 4

---
Basics
- Initial features = 24
- Growth rate k = 12

---
Blocks
- Conv block: Batch Norm, ReLU, Conv2D (3x3)
- Dense block: concatenate input and output of Conv block
- Transition block: Batch Norm, ReLU, Conv2D, (1x1), AveragePooling (2x2, stride 2)
- Theta — some reduction values, in the range (0, 1).

---
Intuition
- DenseNet improves a flow of information and gradients throughout the network, which makes them easy to train
- Each layer has direct access to the gradients from the loss function and the original input signal, leading to an implicit deep supervision.

---
Demo

---
Q & A

---
Fast DenseNet